LjunggrenAudio RYO ADDA
An ADC/DAC in 14hp

Quickstart – what is the ADDA and how do I get going?

An advanced build ADC/DAC with internal clock and external clock option specifically tuned to Eurorack voltages in a 14hp module. No calibration required.

ADDA was designed as a highly experimentalcreative tool and signal processor with good precision, high input impedance and buffered outputs. It will also work great with audio.

Basic specifications
Width: 14hp
Depth with power cable attached: Less than 45 mm.
Power: +/- 22 mA

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!

After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module

The ADDA Kit is a more advanced build and not recommended for novices, it is a high part-count, triple-PCB build that requires more than basic experience in PCB soldering and module assembly. blank blank blank blank blank.

It works as both an ADC and DAC, the left-hand side converting from analog to 8 bit digital, whilst the right hand side converts digital back to analog.
With optional external clocking as well as internal crystal clock.

You can convert pretty much any eurorack signal from analog to digital or vice versa and by combining the two conversions with other processing the results possible are immense.

Any voltage presented to the analog input will cause the module to generate a corresponding digital signal set at the digital outs 1-8 which corresponds to that voltage as per 8bit encoding where +10V is maximum and -10V the minimum. A digital code corresponding to maximum at the 8bit digital inputs (1-8) will cause the analog output to output +10V and corresponding voltages are output down to a mijmum of -10V as per encoding and clock settings the clock is normalled to derive all required signal internally if no external clock aignal is applied, the normalled connection being broken when an external signal is supplied to the clock in socket.

The module can be used as a basic ADC to produce voltage addressed sequencing in a similar but more complex version of the behaviour of RYO VC_Seq and RYO Paths modules; the module can produce a continuous output voltage that varies depending on input digital coding or; both halves can be used together with anything within appropriate ranges as per spec sheet to do an immense variety of creative processing; by patching a signal to any input channel the individual outputs generally will when clocked (internally or externally) produce some form of output.

lank blank blank blank blank blank.
Dimensions

Height:	3U (128.5mm)
Width:	14HP (71.30mm)
Depth:	50mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	22mA
-12V rail	22mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	0V to +10V

Max gain	0dB (1.0x) gain per channel

Nominal impedances
Audio signal input:	22k ohm
Audio Signal output:	in loop compensated
CV input:	n/a

Patch ideas:

Although uses of mixers in patch examples and ideas are found readily online and in some books, and similarly those familiar with using attenuators will be familiar with the basics, there are other less obvious ways to use the ampmix in patches in your modular rig:

below i've include some inspiring words to encourage other patches that might be tried; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Overdrive other modules;
many modules can be fed a hot signal to overdrive the input stage	giving a nice distortion or warm tonality – this is especially true	for VCAs, filters and some mixers.

Boost/attenuate less commonly varied signal;
not only commonplace signals like the main audio in an output chain	or the end output of a patch might need boosting if gain is low,	also try boosting as well as attenuating FM modulators, AM	modulators and other secondary waveforms in a patch so that the	resulting sound output from a carrier VCO/VCF/VCA is different.