LjunggrenAudio RYO Brit_EQ5
A 5-Band British Style EQ in 4hp

Quickstart – what is the Brit_EQ5 and how do I get going?

An easy to build 5-Band Equaliser with overdrive available at high gain and ability to completely defeat any frequency band as well as boost in a 4hp module. No calibration required.

Brit_EQ5 was designed as a handy EQ for mixing and processing audio with good precision, high input impedance and buffered outputs. It could be upgraded for even better precision as described in the assembly manual. It will also works with CV (results may vary).

Basic specifications
Width: 4hp
Depth with power cable attached: Less than 35 mm.
Power: +/- 22 mA

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!

After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module

The Brit_EQ5 Kit is a novice-friendly project, it is a low part-count, single-PCB build that only requires the most basic experience in PCB soldering and module assembly. blank blank blank blank blank.

It works as a 5 channel EQ,
A signal booster with a small gain available at cost of lowered fidelity,
or a versatile frequency sculpting tool.
With up to ?dB gain (/) on each channel.

Brit_EQ5 is small and cheap enough to be racked in multiple channel strips as a channel insert mixer or mixdown channel EQ in a modular multi-channel mixer.

It is equally at home being used more as a color effect to shape sounds as part of a larger processing setup.

A slight gain greater then 1.0x can be achieved by turning the output gain knob past (xdB) so generating an overdiven character to the tone which due to the emulation of vintage British mixer style gyrator circuits is often considered pleasing to the ear. Turning individual frequency channels fully counter clockwise (ccw) will defeat the channels completely allowing no sound in that frequency band to pass, whilst turning the knob for a frequency band fully clockwise will result in an a gain in level dictated by the setting of the output gain knob (maximum +?.0x gain) when all channels at amximum and output gain maxed, however to stay within clean tone output, bear in mind the bands are summed by a mixer, level dictated by output gain knob such that this may have to be decreased.to avoid undesirable rrsults, channels for which no alteration in tone is required should be set to center (1.0x or 0.0dB) is advisable for a clean mix.

The module can be used as a basic attenuator; by patching a signal to the input, centering all channnels and taking its output from the out whilst keeping gain between fully CCW and center as desired.

lank blank blank blank blank blank.
Dimensions

Height:	3U (128.5mm)
Width:	4HP (20.15mm)
Depth:	35mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	22mA
-12V rail	22mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	0V to +10V

Max gain	0dB (1.0x) gain per channel

Nominal impedances
Audio signal input:	22k ohm
Audio Signal output:	in loop compensated
CV input:	n/a

Patch ideas:

Although uses of mixers in patch examples and ideas are found readily online and in some books, and similarly those familiar with using attenuators will be familiar with the basics, there are other less obvious ways to use the ampmix in patches in your modular rig:

below i've include some inspiring words to encourage other patches that might be tried; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Overdrive other modules;
many modules can be fed a hot signal to overdrive the input stage	giving a nice distortion or warm tonality – this is especially true	for VCAs, filters and some mixers.

Boost/attenuate less commonly varied signal;
not only commonplace signals like the main audio in an output chain	or the end output of a patch might need boosting if gain is low,	also try boosting as well as attenuating FM modulators, AM	modulators and other secondary waveforms in a patch so that the	resulting sound output from a carrier VCO/VCF/VCA is different.