LjunggrenAudio RYO DP_Switch
A Dual Patch-Progammable Performance Bi-Direcfional Switch in 6hp

Quickstart – what is the DP_Switch and how do I get going?

An easy to build dual switch with both momentary and latching modesallowing a variety of toggles, flipflops and latches in a 6HP module. No calibration required.

DP_Switch was designed as a handy multipurpose programmable switch and logic processor with good precision, high input impedance and buffered outputs. It could be upgraded for even better precision as described in the assembly manual. It will also work great with CV.

Basic specifications
Width: 6hp
Depth with power cable attached: Less than 35 mm.
Power: +/- 22 mA

Installation

To begin installation, please make sure that:
- you have a standard pinout eurorack bus board
- you have +12V and -12V power rails on that bus board [no +5V supply is required]
- the power rails are not overloaded

!!!Before installing this module disconnect the power from your system!!!

- Double check the polarity of the ribbon cable - The red stripe should be aligned with the -12V rail, on both the module and on the bus board

[we use shrouded headers but it's still possible a cable has been assembled with the stripe on the wrong side of the shroud so always double check!].

Also make sure when using busboards without shrouded headers that the pins aren't transposed a row vertically or horizontally – all pins should insert into holes on the cable.

Although we use both fuses and schottky diodes to provide reverse polarity and excess current protection, we do not take any responsibility for damages caused by wrong power supply connection!

After you have connected everything, double checked it and ensured your case is closed such that no power lines can be touched by your hand or any stray cables drop into holes, turn on your system and test the module

The DP_Switch Kit is a novice-friendly project, it is a low part-count, dual-PCB build that only requires the most basic experience in PCB soldering and module assembly. blank blank blank blank blank.

It works as a dual channel momentary bi-directional switch,
a dual latching bi-directional switch attenuvertor,
1 latching and one momentary bi-directional switch, or
a singular complex switch as dictated by specific patch-programming.

Patch-programmability is a feature defined by a module's ability to perform different functions depending how various features are switched or patched to eachother via patch-cables. If you connect certain outs to certain ins you can get greater functionality than the bsic minimum, building up more complex behaviours depending upon the speciics of the connections made..

An CV routed through one switch and hence controlled in it's routing by the CV input socket for that channel can be routed to, for example the CV input of the other channel so depending on momentary/latching/feedback-loop setups can create complex flip-flops and more besides.

The module can will recognise any Eurorack signal, be it CV, audio or Gate/Trigger; a schmitt trigger on the input turning any rising edge greater than +1V as activation crossing necessary threshold voltage, regardless of contour/waveform shape.

lank blank blank blank blank blank.
Dimensions

Height:	3U (128.5mm)
Width:	6HP (31.00mm)
Depth:	35mm (with power cable attached)

Weight:	???g

Current consumption
+12V rail	22mA
-12V rail	22mA
+5V rail	no +5V supply required

Basic specifications
total frequency controllable range	dc to 50kHz
max input/output audio signal	20Vpp
CV input range	0V to +10V

Max gain	0dB (1.0x) gain per channel

Nominal impedances
Audio signal input:	22k ohm
Audio Signal output:	in loop compensated
CV input:	n/a

Patch ideas:

Although uses of mixers in patch examples and ideas are found readily online and in some books, and similarly those familiar with using attenuators will be familiar with the basics, there are other less obvious ways to use the ampmix in patches in your modular rig:

below i've include some inspiring words to encourage other patches that might be tried; and, as ever, experiment – RYO modules are designed with all necessary protection and fail-safes so you can just start plugging in patch cables and see what happens!

Overdrive other modules;
many modules can be fed a hot signal to overdrive the input stage	giving a nice distortion or warm tonality – this is especially true	for VCAs, filters and some mixers.

Boost/attenuate less commonly varied signal;
not only commonplace signals like the main audio in an output chain	or the end output of a patch might need boosting if gain is low,	also try boosting as well as attenuating FM modulators, AM	modulators and other secondary waveforms in a patch so that the	resulting sound output from a carrier VCO/VCF/VCA is different.